INSTR	O1_typeselect	O2_typeselect	O1_regselect	O2_regselect	ALU_O2_typeselect	decidion_make	clock_control	write_type	write_enable	jump_enable	MOV_instr	mem_flush	mem_write_ctrl	20-bit_instr_in_hex	compressed_Instruction_8-bit
IDLE	00	00	00	00	00	00	10	0	0	0	0	0	0	0x00080	0x00
SEL r0,r1	01	10	00	01	01	00	11	0	0	0	0	0	0	0x614C0	0x10
SEL r0,r2	01	10	00	10	01	00	11	0	0	0	0	0	0	0x624C0	0x11
SEL r0,r3	01	10	00	11	01	00	11	0	0	0	0	0	0	0x634C0	0x12
SEL r1,r0	01	10	01	00	01	00	11	0	0	0	0	0	0	0x644C0	0x13
SEL r1,r2	01	10	01	10	01	00	11	0	0	0	0	0	0	0x664C0	0x14
SEL r1,r3	01	10	01	11	01	00	11	0	0	0	0	0	0	0x674C0	0x15
SEL r2,r0	01	10	10	00	01	00	11	0	0	0	0	0	0	0x684C0	0x16
SEL r2,r1	01	10	10	01	01	00	11	0	0	0	0	0	0	0x694C0	0x17
SEL r2,r3	01	10	10	11	01	00	11	0	0	0	0	0	0	0x6B4C0	0x18
SEL r3,r0	01	10	11	00	01	00	11	0	0	0	0	0	0	0x6C4C0	0x19
SEL r3,r1	01	10	11	01	01	00	11	0	0	0	0	0	0	0x6D4C0	0x1A
SEL r3,r2	01	10	11	10	01	00	11	0	0	0	0	0	0	0x6E4C0	0x1B
SEL r0,mem	01	11	00	00	10	00	11	0	0	0	0	0	0	0x708C0	0x1C
SEL r1,mem	01	11	01	00	10	00	11	0	0	0	0	0	0	0x748C0	0x1D
SEL r2,mem	01	11	10	00	10	00	11	0	0	0	0	0	0	0x788C0	0x1E
SEL r3,mem	01	11	11	00	10	00	11	0	0	0	0	0	0	0x7C8C0	0x1F
MOVR r0,imm	01	00	00	00	00	00	11	0	0	0	1	0	0	0x400C4	0x20
MOVRr1,imm	01	00	01	00	00	00	11	0	0	0	1	0	0	0x440C4	0x21
MOVR r2,imm	01	00	10	00	00	00	11	0	0	0	1	0	0	0x480C4	0x22
MOVR r3,imm	01	00	11	00	00	00	11	0	0	0	1	0	0	0x4C0C4	0x23
MOVM r0	01	00	00	00	00	00	11	0	1	0	0	0	1	0x400D1	0x30
MOVM r1	01	01	00	00	00	00	11	0	1	0	0	0	1	0x500D1	0x31
MOVM r2	01	10	00	00	00	00	11	0	1	0	0	0	1	0x600D1	0x32
MOVM r3	01	11	00	00	00	00	11	0	1	0	0	0	1	0x700D1	0x33
WE zr	00	00	00	00	00	01	11	0	0	0	0	0	0	0x001C0	0x40
WE gf	00	00	00	00	00	10	11	0	0	0	0	0	0	0x002C0	0x41
WE lf	00	00	00	00	00	11	11	0	0	0	0	0	0	0x003C0	0x42
JMP imm8	00	00	00	00	00	00	11	0	1	1	0	0	0	0x000D8	0x50
JE imm8	00	00	00	00	00	01	11	0	1	1	0	0	0	0x001D8	0x60
JG imm8	00	00	00	00	00	10	11	0	1	1	0	0	0	0x002D8	0x70
JL imm8	00	00	00	00	00	11	11	0	1	1	0	0	0	0x003D8	0x80

ALU opcodes (to be used in combination with sel instruction). Equivalents of x86 asm are quoted

opcode	ALU function
0x1	ADD
0x2	subtract
0x3	multiplication
0x4	division
0x5	Compare. Same as CMP in x86. Sets the flags accordingly.
0x6	Shift left logical (SHL O1,O2)
0x7	Shift right logical (SHR O1,O2)
0x8	Shift Arithmetic Right (SAR O1,O2)
0x9	Rotate left (ROL O1,O2)
0xA	Rotate right (ROR O1,O2)
0xB	AND O1,O2
0xC	OR O1,O2
0xD	XORO1,O2
0xE	NOT O1